## Slide 1: HCS12 Project Stationary for Metrowerks Code Warrior

## Slide 2: Stationary Overview
Friendly software development environment to tackle market-demanding applications
Project architecture that focuses on both the customer and internal personnel
Supports a growing number of HCS12 microcontrollers by including all necessary files
Designed to assist with New Product Introduction (NPI)

## Slide 3: Stationary Concept
Based on part name and mask set to keep track of product revisions
Peripheral files only include modules pertaining to part name in order to support System on Chip (SoC) ideology
Module structure definition files follow strict naming convention to coincide with document name

## Slide 4: Software Hierarchy
Application Software
Project Globals
Drivers
Peripheral Files
Structure Definitions
Arrow direction
represents include
Project Vectors
Structure defs
Included through Project Globals

## Slide 5: Software Architecture # 1
Application Software – source code controlling external application
Project Globals – source code interfacing application software with respective module drivers and peripheral / structure definitions, depending on part / mask set.
Project Vectors – predefined dummy interrupt vector handlers

## Slide 6: Software Architecture # 2
Drivers – source code routines to initialize and build application software.
Peripheral Files – source code identifying peripheral modules included in specific Part / Mask set. Also, defines register locations.
Structure Definitions – source code defining register structures down to the bit level.

## Slide 7: Supported Parts
DP256
  0K79X
  1K79X
A256
  1K79X
H256
  0K78X
DT128
  0L85D
D64
  0L86D
Ram, Flash, and Banked_Flash Target Applications are supported per part
DP512
  0L00M
A128
  0L85D
E128
  0L08M
C32
  0L45J

## Slide 8: HCS12 Project Stationary for Metrowerks Code Warrior
~ User’s Guide ~

## Slide 9: How to open the stationary?
Download latest HCS12_Stationary.zip
  http://compass.mot.com/go/hcs12stationary
Extract stationary into any directory
  Stationary will form structured directory labeled S12_Projects
Open _MC9S12.mcp project file to get started
  File located within S12_Projects\_MC9S12\ directory
Notes: Download, Extract, Open

## Slide 10
http://compass.mot.com/go/hcs12stationary
Click to download
Notes: Download latest updated HCS12 Project Stationary from WWW.

## Slide 11
Extract
Open
Double-click to open Project window
Downloaded Zip File
Notes: Extract stationary and open project file

## Slide 12
Main project stationary window displaying all necessary global, source, peripheral, parameter, and definition files to develop your application
To include a file into the compilation, click under the red bulls eye column next to the desired file (included file is marked by a bullet)
Red bulls eye column
Notes: Main Project Stationary Window

## Slide 13: How to select a part?
First, open projectglobals.h (within the Globals folder in the main project window) and uncomment only the desired part for your application under the Mask Set selection box. (Step 1)
Second, select the peripheral file (within the Peripherals folder in the main project window) respective to the desired part for your application. (Step 2)
Third, select the parameter file (within the Prm folder in the main project window) respective to the desired part for your application and the selected build target (Ram,Flash,Banked_Flash) (Step 3)
Notes: Defining the 3 steps to setting up a project for a specific part.

## Slide 14
Step 1: Include a Part and Mask Set
Double-click to open projectglobals.h
Within projectglobals.h, uncomment the part and mask set for your application by removing “ // ” before #define statement
Notes: Step 1 for selecting part and mask set

## Slide 15
Step 2: Include a Part’s respective Peripheral File
Click under the red bulls eye column next to the desired file (included file is marked by a bullet)
Example above includes per_DP256_1K79X.c file indicated by the bullet
Notes: Step 2 for selecting appropriate peripheral file to include per part/maskset

## Slide 16
Step 3: Include a Part’s respective Parameter File
Click under the red bulls eye column next to the desired file (included file is marked by a bullet)
Example above includes _MC9S12DP256.prm file indicated by the bullet
Note: Only select a *.prm file matching the build target
RAM.prm  Ram Application
FLAT.prm  Flash Application
BANKED.prm  Banked_Flash
Select Build Target
Notes: Step 3 for selecting matching parameter file per part and build target

## Slide 17: How to begin your application?
Open blank main.c (within Sources folder in the main project window) and enter your source code
Example source code
Notes: Example source code showing how to begin your application

## Slide 18: How to implement interrupt vectors?
Open projectvectors.c
First, open projectvectors.c (within the Globals folder in the main project window) and enter your Interrupt Service Routine Function within the appropriate interrupt routine.
Within projectvectors.c you will find predefined interrupt vectors for all supported parts. Just add your interrupt service routine as a function (ex. Dummy_handler ();) within the appropriate interrupt routine

## Slide 19
Insert interrupt service function
inside Interrupt Service Routine
Note: Only the ISR within projectvectors.c starts with the “interrupt” typedef
Notes: Example showing how to properly insert an interrupt service routine using the project stationary

## Slide 20: Questions